## Slide 1
HVAC · TAKE-HOME ASSESSMENT · 2026
Arjun Sarath
Ductline
Drawing in. Structured duct data out.
V1
→
V2
→
V3
→
PRODUCTION
SUBMISSION
AUTHOR
Arjun Sarath
SCOPE
16-slide narrative · 5-drawing benchmark
REPO
implementation/ · V1, V2, V3 all building

## Slide 2
Ductline · Drawing in. Structured duct data out.
02 / 17
CONTENTS
I · THE PIVOT STORY
02
Engineers re-key duct data by hand.
03
One page in. Every duct out.
04
Three architectures attempted.
05
V1 · One VLM call. Six deterministic stages.
06
Why V1 is parked.
07
V2 · Built. Iterated. Decline observed.
II · V3 IN PRODUCTION
08
V3 · Replace the model with a click.
09
V3 results · 3 of 5 production-quality.
10
V3 · What the user sees.
III · ROADMAP
11
Defending the pivots.
12
Production timeline.
13
Path to full automation.
14
Track 02 · Fine-tuned VLM.
IV · DEFENSIBILITY
15
Three commitments behind the build.

## Slide 3
Ductline · Drawing in. Structured duct data out.
02 / 16
01 · THE PROBLEM
Engineers re-key duct data by hand.
Every drawing. Every job. Across estimating, fab, and as-builts.
8–40
sheets per estimating set
Each sheet re-typed downstream into pricing models, fabrication cut lists, and as-built records. No structured pass between formats.
WHO PAYS FOR IT
Estimators
~6–10 hours / project re-keying ducts into pricing sheets.
12h
Fabricators
Re-reading dimensions a second time to build cut lists.
2×
Owners
As-builts rebuilt from PDFs, then misplaced at audit.
0%
The wedge — drawing → structured duct data.

## Slide 4
Ductline · Drawing in. Structured duct data out.
03 / 16
02 · THE SOLUTION
One page in. Every duct out.
Color mask · skeleton · OCR attribution · SMACNA pressure class.
INPUT
HVAC drawing
Single-page PDF or PNG. Plan view, title block, schedule, legend.
PDF · PNG · JPG
→
PIPELINE
Deterministic CV
Color mask · skeleton · OCR token attribution. No LLM in the hot path.
REASONING TRACE PER DETECTION
→
OUTPUT
Duct records
Geometry · dim · pressure class · confidence · evidence. One JSON per segment.
COST · CUT LISTS · AS-BUILTS
Five benchmark drawings · color-coded outlines · parallel-wall plans.
NO LLM IN THE HOT PATH · FULLY ON-PREM

## Slide 5
Ductline · Drawing in. Structured duct data out.
04 / 16
03 · ARCHITECTURE EVOLUTION
Three architectures attempted.
The order matters — V3 looks the way it does because of what V1 and V2 surfaced.
V1
PARKED
Hybrid VLM + CV
VLM region detection + deterministic refinement. Seven stages.
BUILT
Yes — end to end
BET
11B vision model
RESULT
Structural failure
V2
PARKED
Reviewer + Tiled
Page categorizer, tiled VLM calls, neighbour context, reviewer loop.
BUILT
Yes — full loop
BET
Layers compensate
RESULT
Decline observed
V3
SHIPPING
Color-driven CV
User picks duct color. HSV mask → skeleton → OCR → SMACNA. No VLM.
BUILT
Live · iterative
BET
Skip the model
RESULT
3 / 5 production

## Slide 6
Ductline · Drawing in. Structured duct data out.
05 / 16
04 · V1 · HYBRID VLM + CV
One VLM call. Six deterministic stages.
The bet was a single agent stage gated by typed tool calls — everything else algorithmic.
01
Ingest
ALG
02
Quality
ALG
03
Region
ALG
04
Detect
AGT
05
Extract
ALG
06
Classify
WF
07
Assemble
ALG
Detect is the only agent stage.
ALG
algorithmic
AGT
agent · VLM tool call
WF
workflow
THE BET
An open-source 11B vision model emits structured duct bboxes; OpenCV refines geometry. CV-only fallback if the call fails.
WHAT SURVIVES
VLMClient Protocol + DetectDuctsTool typed schema. ADR-0002 — switching to a frontier model is a config flip.

## Slide 7
Ductline · Drawing in. Structured duct data out.
06 / 16
05 · WHY V1 IS PARKED
The bet was the VLM. It didn’t pay off.
Five-drawing benchmark. Failure modes are structural, not bugs.
FAILURE MODE
FREQUENCY
ROOT CAUSE
Malformed JSON from VLM
4 / 5
11B vision models can’t reliably emit structured JSON.
Hallucinated regular-grid bboxes
2 / 5
Model parrots its training-distribution prior — web charts.
Ollama timeout (≥ 3 min)
1 / 5
Vision pass exceeds soft latency budget on commodity hardware.
CV fallback over-recalls
5 / 5
HoughLinesP fires on walls, columns, gridlines without OCR gating.
On-prem × open-source VLM = unwinnable today.
11B isn’t enough · 90B is too slow on commodity hardware · frontier proprietary can’t run on-prem.

## Slide 8
Ductline · Drawing in. Structured duct data out.
07 / 16
06 · V2 · REVIEWER + TILED DETECTION
Built. Iterated. Decline observed.
V2 added the layers V1 was missing. Accuracy went down. Latency went up.
WHAT V2 ADDED
Designed enhancements, fully built on V1.
Page categorizer
Plan view · schedule · notes.
Tiled detection
1100 px tiles · 15% overlap · trail context.
Reviewer agent
Second-pass critique on low-confidence segments.
Legend parser
Symbols + abbrevs grounded into the detector.
Smart per-tile DPI
Re-render so dim text reaches OCR-readable size.
WHAT WE OBSERVED
Each new VLM call added new failure surface.
END-TO-END ATTRIBUTION
↓
on 3 / 5 drawings vs V1
PER-DRAWING LATENCY
+8–14×
30 s → 4–7 minutes (page-tiled)
REVIEWER-LOOP VALUE
≈ 0
no precision lift; oscillates

## Slide 9
Ductline · Drawing in. Structured duct data out.
08 / 16
07 · V3 · COLOR-DRIVEN DETERMINISTIC
Replace the model with a click.
The user already knows which lines are ducts — they’re color-coded. Don’t ask the VLM to redo work the engineer already did.
01
Color pick
Click duct color.
02
HSV mask
Flood-fill interior.
03
Skeleton + DT
Centerline · half-width.
04
OCR + regex
AxB · A″Ø · CFM.
05
Attribution
Token → its duct.
06
Calibrate ppu
Histogram of pix/in.
07
SMACNA class
Pressure when flow present.
THE TRADE
One click per duct system.
Color-coded plans dominate commercial sets. Schedules cite the same legend.
THE WIN
Real results today.
3 of 5 benchmark drawings produce trustworthy widths in < 5 seconds per page.

## Slide 10
Ductline · Drawing in. Structured duct data out.
09 / 16
08 · V3 RESULTS · 5-DRAWING BENCHMARK
3 of 5 production-quality. 2 of 5 partial.
Pixel-width accuracy split by drawing convention. Numbers are segments correctly attributed.
DRAWING
CONVENTION
MODE
SEGMENTS
WIDTH ACCURACY
01 · afdb-clean-cad
Saturated colored outlines
OUTLINE
25
100%
02 · newwest-mixed-trades
Black closed outlines + callouts
OUTLINE
20
90%
03 · caddsultants-shop
Saturated colored outlines
OUTLINE
35–60
85%
04 · asc2018-bid-set
Parallel-wall dark ducts
CENTERLINE
10
attr ok · width ✗
05 · federal-attachment
Parallel-wall dark ducts (dense)
CENTERLINE
58
attr ok · width ✗
Drawings 04 – 05 attribute correctly · pixel-width fails.
On parallel-wall plans, mask thickness is dilation, not duct gap. Closed by OCR-anchored Pattern A (M1–M2).

## Slide 11
Ductline · Drawing in. Structured duct data out.
10 / 16
09 · V3 · WHAT THE USER SEES
Pick a color. Get a result. Click for the trace.
Reasoning surfaced in-line. Cursor magnifier · 140 px · 6× zoom. Per-segment cards: dim, pressure class, confidence.
LIVE INTERFACE
Color picker
User clicks a duct color in the legend or on the plan.
Overlay
Transparent PNG masks rendered over the page.
Segment cards
Dim · pressure class · confidence per duct.
Reasoning trace
Click any segment for attribution rule + ppu source.
Magnifier
140 px · 6× zoom on hover for pixel-level checks.

## Slide 12
Ductline · Drawing in. Structured duct data out.
11 / 16
10 · DEFENDING THE PIVOTS
Why didn’t they just stay on V1?
Three load-bearing claims for future contributors.
01
V1 → V2 wasn’t enough.
V2 added the missing layers. Built end-to-end. Accuracy down. Latency up.
Compounded an unreliable signal.
02
V1 → V3 was correct.
V3 removes the failure mode. The user names the color. Downstream is deterministic.
Trade: one click. Win: 3 / 5 today.
03
V3 isn’t the final form.
Doesn’t yet handle parallel-wall ducts. Requires manual color pick. Roadmap closes both.
Custom model replaces the pick.

## Slide 13
Ductline · Drawing in. Structured duct data out.
12 / 16
11 · PRODUCTION TIMELINE
Standards-based milestones.
Each milestone — handles drawings of standard X in Y months. Pace assumes V3’s shipping cadence.
M0
M2
M4
M6
M8
M10
M12
Y2
V3 alpha · M0
Color-coded · 3 / 5
OCR-anchored Pattern A · M1–M2
Parallel-wall · 5 / 5 target
Schedules · M3–M4
Equipment + room
Multi-page · M5–M6
8 – 40 sheet sets
Auto-detect color · M7–M9
No manual pick
Confidence calibration · M10–M12
200–500 corpus
Custom model · YEAR 2
CAVEATS
2–3 weeks build + 1 week iteration per milestone · one engineer FT on detection · part-time front-end + ops · customer-pilot drift can push by a multiple.

## Slide 14
Ductline · Drawing in. Structured duct data out.
13 / 16
12 · PATH TO FULL AUTOMATION
Three improvement tracks.
Out-of-the-box VLMs already failed. Forward path is fine-tuning.
TRACK 01
M0 → M6
V3 deterministic wins
OCR-anchored Pattern A
Pattern A auto-detection
Schedule + legend extraction
Confidence calibration
Multi-page topology
1 engineer FT · 6 months
TRACK 02
YEAR 2
Fine-tuned VLM, in parallel
Out-of-box Claude / GPT-4o failed
Path A — fine-tune Claude / GPT-4o
Path B — open-source LoRA
Same eval, both paths
Migrate to OSS once it wins
Shared corpus · ~$30–80K · 6–9 mo
TRACK 03
YEAR 2 H2
Custom detection model
Faster R-CNN · FPN backbone
1K–5K labeled drawings
$30–80 / drawing labeled
$5–10K compute · 3–4 mo
Replaces the picker UX
Data-bound · 9–12 months

## Slide 15
Ductline · Drawing in. Structured duct data out.
14 / 16
13 · TRACK 02 · FINE-TUNED VLM
Two fine-tune paths. One shared corpus.
Out-of-the-box Claude · GPT-4o · llama3.2-vision all failed on engineering drawings.
PATH A · PROPRIETARY FINE-TUNE
Fine-tune Claude or GPT-4o vision.
VENDOR APIS
Anthropic / OpenAI vision fine-tune programs
WHY FIRST
Highest-capacity base · fastest to clear the bar
TRIGGER
Customer can ship drawings off-prem
COST
Per-token API · ≈ $0.05 – $0.15 / page
PATH B · OPEN-SOURCE LORA
Open-source vision + LoRA on same data.
BASE
Llama 3.2 Vision · Qwen2-VL · DeepSeek-VL
ADAPTER
LoRA · 4-bit quant on 24 GB GPU
WHY PARALLEL
Same training data — funding both is incremental
ON-PREM
Defence, gov, AEC firms that can’t ship to a vendor
Convergence — when the OSS fine-tune outperforms on the same eval, migrate to OSS only. Lower cost · on-prem · no lock-in.

## Slide 16
Ductline · Drawing in. Structured duct data out.
15 / 16
14 · TRACK 03 · CUSTOM MODEL
Purpose-trained detector replaces the picker.
Pressure class, dim attribution, and SMACNA logic stay downstream of detection — unchanged.
Faster R-CNN
ARCHITECTURE
FPN backbone · calibrated
5K
LABELED DRAWINGS
Customer-contributed
$30–80
PER DRAWING
Technical labelers
$5–10K
TRAINING COMPUTE
5K corpus · A100 hours
WHAT IT REPLACES
Just the user’s color-pick step.
Upload → segments. No picker. Pressure class, dim attribution, SMACNA — unchanged. V3 deterministic stays as fallback.
RISKS TO WATCH
Distribution shift on new customers.
Confidence calibration in detectors.
V3 must stay green for fallback.

## Slide 17
Ductline · Drawing in. Structured duct data out.
16 / 16
15 · WHAT MAKES THIS DEFENSIBLE
Three commitments behind the build.
01
Algorithmic-first.
Deterministic where possible. The VLM is one config flip away — the pipeline isn’t built around it.
02
Honest confidence.
Calibration cross-validates extracted dims against measured pixels. We never claim ‘high’ for a value we didn’t OCR.
03
Reasoning surfaced.
Every detection carries its trace — attribution rule, ppu source, pressure source. The user sees what the system saw.
Ductline.
Drawing in. Structured duct data out.
V3 ALPHA SHIPPING · M0–M6 CLOSES THE DETERMINISTIC GAPS · YEAR 2 CLOSES THE MODEL GAP.

## Slide 18
Ductline · Drawing in. Structured duct data out.
17 / 17
Thank you
CONTACT
AUTHOR
Arjun Sarath
REPO
implementation/ · V1, V2, V3
V3 ALPHA SHIPPING · ROADMAP DEFINED.